## Slide 1: Energy Optimal Control of a Towing Kite
Project Group 1.3
Ashwin Nedungadi - 230397
Mehmet Batu Özmeteler - 230306
Rajesh Pushparaj - 229981

## Slide 2
Introduction

## Slide 3: What is Model Predictive Control (MPC)?
an advanced control method
uses a model to predict the future behavior of a controlled system over a finite time horizon
computes an optimal control input according to a performance criterion

## Slide 4: Working Principle
Measure or estimate state information
Compute a sequence of optimal control inputs over a prediction horizon N
Apply the first part of the optimal trajectory
Shift the horizon and repeat

## Slide 5: Pros and Cons
can satisfy constraints
can handle MIMO systems
requires large memory and computationally expensive

## Slide 6
Problem Formulation

## Slide 7: Problem Statement
Dynamic System: a towing kite that is to be used to save the fuel of seagoing vessels
Goal of the Controller: maximize the harvested wind energy while satisfying the minimum height constraint

## Slide 8: System Overview
Simplified System Vectors
Non-linear Dynamic Model

## Slide 9: System Overview
Glide Ratio and Relative Wind Speed
Tether Force and Kite Height

## Slide 10: OCP Formulation
for a smooth
control trajectory
for orthogonal
collocation
slack variable for the soft constraint implementation
the minimum height constraint
state and input constraints
maximizes the
tether force

## Slide 11: Tuning Parameters

## Slide 12
Numerical Implementation

## Slide 13
Define the system and problem parameters and import the wind_model.py
Define the system dynamics as a CasADi function and create an ODE solver
Implementation

## Slide 14
Generate collocation points, find the collocation coefficients and continuity coefficients

## Slide 15
Formulate the tether force and define the stage cost as a CasADi function
Define height constraint as a CasADi function
Set the lower and upper bound for states, input and slack variable

## Slide 16
Add the stage cost for the prediction horizon and add the discretized system constraints

## Slide 17
Create the MPC solver using the CasADi function nlpsol
Set initial conditions and initial guesses to solve the open-loop prediction
Use the solution obtained from the open-loop prediction as the initial guess for the MPC loop
Solve the optimization problem with a receding horizon scheme
Store the states and input for each iteration

## Slide 18
Results

## Slide 19: Kite Trajectories

## Slide 20: Control Input

## Slide 21: Open-Loop vs. Closed-Loop
Kite Trajectories with Different Constant Relative Wind Speeds – Open-Loop
Kite Trajectories with Different Varying Relative Wind Speeds – Closed-Loop

## Slide 22
THANK YOU FOR LISTENING!